### Problem Statement: Calculating the Temperature Profile of a Protoplanetary Disk

Objective:
Write a Fortran program to calculate the temperature profile of a protoplanetary disk as a function of distance from the central star. The disk's temperature is crucial in understanding planet formation processes.
Background:
The temperature T(r) of a protoplanetary disk often follows a power-law profile:
T(r)=T0(r0/r)^(−q)
where:
- T0​: Temperature at a reference distance r0​ from the star (usually taken as 1 AU).
- r: Distance from the star in AU.
- q: Power-law index, which typically ranges between 0.5 and 1.0 for protoplanetary disks.
Tasks:
1. Define the reference temperature T0​ and reference distance r0​.
2. Allow the user to input the values of T0​, q, and the range of distances r from the star.
3. Compute the temperature profile over the specified range.
4. Output the results in a tabular format showing the distance and corresponding temperature.
5. Bonus: Plot the temperature profile using data output (if you want to visualize it later with Python or another tool).
Hints:
- Use arrays to store distances and corresponding temperatures.
- Implement error handling for invalid inputs (e.g., negative distances or unrealistic temperatures).
- Ensure your code is modular by using subroutines/functions where appropriate.